## Slide 1
Ferrous Metals contain iron and are magnetic and rust |  | 
Material | Key info | Examples
Low Carbon Steel | Tough and ductile and easily machined and welded | Construction, screws, cars
High Carbon Steel | Hard and wears well | Tools, blades and knives
Cast Iron | Hard but brittle. Easily cast but hard to machine | Pots, pans, vices
Non-Ferrous Metals do not contain iron, aren’t magnetic and don’t rust |  | 
Material | Key info | Examples
Aluminium | Light, high strength to weight ratio and ductile | Pots, pans, cars, cans
Copper | Ductile, malleable and good conductor | Plumbing supplies and cables
Tin | Soft, malleable and good conductor | Used as a protective coating
Metals come from ores in the ground. Stock forms are sheets, bars and rods
Alloys are mixtures of 2 or more metals to get the best of their properties |  | 
Material | Key info | Examples
Brass | Malleable and easy to cast | Musical instruments, plumbing
Stainless Steel | Doesn’t rust, hard and smooth | Cutlery, medical tools, etc
Metals are mined from the earth and then go through an extraction process
Extraction happens by putting the ore in a blast furnace
The metal is then separated from the waste material
Metals, Alloys and Plastics
Metals
Alloys
Primary Processing of Metals and Alloys
Plastics come from crude oil. Stock forms are sheets, powders, granules and rods
Plastics
Thermoplastics can be reheated and reshaped and infinite amount of times |  | 
Material | Key info | Examples
PET | Easily blow moulded, food safe and easily recycled | Bottles, packaging, etc
PVC | Flexible, tough, easily extruded | Pipes, tape, hard hats
HIPS | Flexible, lightweight, food safe and easily vacuum formed | Containers and yoghurt pots
Acrylic | Tough, brittle, easily scratched | Car lights, baths, displays/ signs
Thermosets once heated and set cannot be reshaped |  | 
Material | Key info | Examples
Melamine Formaldehyde | Food safe, hygienic, hard and brittle | Kitchenware and work surfaces
Urea Formalehyde | Good insulator, hard and brittle | Electrical casings, buttons and handles
Polyester Resin | Strong, heat resistant, can be transparent | Coatings, casings
Primary Processing of Plastics
Crude oil is extracted from the earth and then processes into different types of fuels, etc. This is called Fractional Distillation
A process called Cracking then converts the large hydrocarbon molecules into plastics