## Slide 1: Level 1/2 Engineering Knowledge Organisers

## Slide 2: Processes, tools and equipment

## Slide 3
Processes vocabulary Knowledge organiser
WJEC Engineering
Preparation
Marking out: using tools (e.g. engineer’s blue, scriber, steel rule)to mark out a material from a plan
Scribing: The process of using a scriber to mark a line onto a workpiece/material
Annealing: heating a metal to change its physical properties which makes it more ductile and easier to work with.
Pg 1 of 1
Finishing: The process of removing swarf, scratches and imperfections from a product after manufacturing.
Polishing: Applying polish to make the material shiny
Sanding: Removing rough or scratched surfaces using sandpaper (wood) or wet and dry paper (metals and plastics)
Painting: applying a paint to a material, which can be water or oil based
Galvanising: Dipping steel into molten zinc to protect it from rusting
Anodising: Dipping aluminium into an acid bath with an electric current flowing through. This is used to add a protective and coloured layer.
Bluing: Dipping steel into hot oil to protect it from corrosion, scratching and reduce glare.
Manufacturing processes (making activities)
Wasting: Processes which remove material
Turning: Using a centre lathe to reduce the diameter of a part
Milling: using a vertical milling machine to cut or shape metal using a rotating tool
Drilling: using a drill bit (on a pillar drill or centre lathe)to remove a circular hole
Filing: removing edges of a material using a file
Cutting: removing part of a material by cutting with a tool e.g. hacksaw, junior hacksaw, tin snips, etc.
Kurling: Adding a textured finish to a cylindrical part using a knurling tool on a centre lathe to provide grip to a part.
Tapering: Reducing the diameter of a part down towards a point.
Quenching: rapidly cooling a metal to change its molecular structure and make it harder
Process: A series of steps within an activity which are followed to achieve an end goal
Fabricating: Processes which join materials
Soldering: Either the joining of electronic components to a PCB (printed circuit board), or the joining of metals by melting a low temperature metal (solder) to create the joint.
Welding: joining metals together using a welding machine which is electrically powered (spot welding/ arc welding/MIG welding/ TIG welding)
Brazing: Joining steel to itself or other metals using a melted lower temperature metal e.g. brass
Joining: joining two materials together using fixings, e.g. nuts and bolts, rivets, etc.

## Slide 4
Marking Gauge
Used for marking a line parallel to the edge of the surface.
Marking out tools Knowledge organiser
WJEC Engineering
Pg 1 of 1
Engineer’s blue
A liquid that can be painted onto a surface of metal that you can scribe through to create a thin line
Engineer’s (tri) square
A tool for scribing 90° lines on a section of material. The stock is placed on the side of the material and the blade rests on top.
Steel rule
Uses for measuring out on flat surfaces. It in has increments of 1 mm.
Steel Scriber
These come in different shapes but are used to mark out metal for machining/ cutting/ drilling etc. The end is made from high carbon steel
Dividers
These work very similarly to compasses but instead of a pencil at one end, there is a scriber at both ends. This enables you to scribe circles onto metal. You must use a centre punch first to help the dividers stay in place at your centre of rotation.
Centre punch
For marking out the centre of a hole to make it ready for drilling. This stops the drill bit from skating around the surface and accidentally drilling in the wrong place. They are used with a hammer.
Key words: Scribing = to mark out
Odd leg Calipers / Jenny Calipers
Used for marking a line parallel to the edge of the surface or circle

## Slide 5
Measuring tools Knowledge organiser
All measuring tools are available in metric (mm) and imperial (inches) but in the UK for Engineering we use metric
WJEC Engineering
Pg 1 of 1
Vernier Callipers
These are used for measuring outer diameters or thickness of objects. The depth bar can also be used to measure the depth of holes. Can also be digital
Internal callipers
Used for measuring internal diameters. These look like dividers but have curved bottoms
Dial Callipers
Works the same as a vernier calliper but shows additional readings on a dial for each 0.2mm increment.
Steel rule
Used for measuring out on flat surfaces. It in has increments of 1 mm or 0.5mm.
Multimeter
A multimeter is a measuring instrument that can measure multiple electrical properties. A typical multimeter can measure voltage, resistance, and current
Micrometer
Is mainly used to measure external diameters and material thickness. They can measure up to a hundredth of a millimeter
Key words:
metric = measurements in millimeters or metres
Tolerance = how much larger or smaller a part is allowed to be
M8 = Metric 8mm. This type of measurements is used for standard sizing, e.g drill bit sizes
M8x0.5 = This is used to show the measurement of a thread: 8mm diameter and 0.5mm thread pitch
Calculating tolerance
25mm +/- 0.5
This means that the 25mm measurement is allowed to be 0.5mm larger and smaller.
25mm + 0.5mm = 25.5mm
25mm- 0.5mm = 24.5mm
External callipers
is used to measure the external diameter of an object, or to measure the thickness of an object
Tape measure
Uses for measuring flat surfaces in metres

## Slide 6
Shaping tools
Cutting tools
Work holding
File
Files are used to square ends, file rounded corners, remove burrs from metal, straighten uneven edges, file holes and slots, smooth rough edges, etc. There are different shaped files: Flat file / round file / square file / etc
Hand tools Knowledge organiser
WJEC Engineering
Pg 1 of 1
Flat vice / machine vice
Screwed to the pillar drill bed and used to hold work whilst drilling on a pillar drill
Hand vice
useful when working on a drilling machine, or working with small parts that need to be clamped together.
Soft jaws
Slotted onto a engineers vice and used to pretect soft metals from imprints from the vice jaws.
G-Clamp
Used for general clamping in the workshop. Can achieve high pressure levels
Quick release G clamp
Used for the same purpose as a G-clamp, but has buttons to allow it to quickly open and close
Hacksaw
The Hacksaw is used for cutting materials, and for cutting away waste parts of the work. Most Hacksaws are made from Low Tungsten Steel or Carbon Steel, however the more expensive blades are made from High Speed Steel. The tension on the blade is formed by the frame.
Engineer’s vice
Attached to a work bench and used to hold work in place
Junior Hacksaw
The Junior Hacksaw is used with a shorter blade on smaller or thinner pieces of material.
Wet and dry paper
This is available in different grades, rough to smooth and is used to sand metal and plastic.
This will remove scratches and bring it to a high shine.
Tin snips
Shaped like scissors, tin snips are used for cutting through thin sheets of metal.
Metal Shears
Shears work by holding the metal in place and applying a downwards force with a blade. This is used to cut large sheets of thin metal.
There are different types available for different sized materials and uses
Shears
Hand shear
Tap and die
These are used for cutting threads into materials to use with bolts and machine screws. Taps and used with a tap wrench to add a thread to a pre-drilled hole and dies with die holders are used to add a thread to the exterior of a cylinder/rod
Tap
Die
Tap wrench
Die wrench/holder

## Slide 7
Centre lathe Knowledge organiser
What is a centre lathe used for?
A centre lathe is used to manufacture mainly cylindrical products/ objects. Lathe can be operated both manually (in the workshop) or using CNC in industry.
Useful websites:
Technology student: centre lathe
BBC bitesize
DT online: centre lathe
Common phrases:
Turning:
Reducing the diameter of a cylindrical object.
Facing off:
Ensuring that the end of a cylindrical object is flat (perpendicular to its sides)
Parting off:
Cutting the workpiece to a specific length with a specific cutting tool (parting tool)
Taper turning:
Creating a taper down the length of the workpiece(think cone-shaped)
Knurling:
Creating a textured surface on your workpiece
Grooving/ face grooving:
Creating a groove on the external diameter or face
Boring:
Enlarging an existing hole in a workpiece using cutting tools or a ‘boring bar’
Fitting tools
The workpiece (material) on a lathe is held in place using a chuck. This uses 3 or 4 jaws to self-centre the workpiece as they come together.
A chuck key is used to tighten the jaws of the chuck.
Safety precautions
A risk assessment must be completed before using this machine.
Safety goggles and apron must be worn.
Long hair must be tied back
Limited persons around the machine e.g. user plus instructor only.
Workpiece must be securely closed in the chuck.
Machine guard must be set to the correct position.
Tools must be sharpened and set up correctly.
Correct machine speed must be selected.
4-jaw centre lathe chuck
Spring loaded chuck key
This has a spring so that it cannot be left in the chuck and cause injury to the user.

## Slide 8
Vertical milling machine Knowledge organiser
WJEC Engineering
What is a vertical milling machine used for?
This machine uses a rotating cutting tool to produce machined surfaces by progressively removing material from a work piece.
The machine vice is controlled using handles to allow it to accurately move along 3 axis. More advance machine can be partly or fully automated.
Safety precautions
A risk assessment must be completed before using this machine.
Safety goggles and apron must be worn.
Long hair must be tied back
Limited persons around the machine e.g. user plus instructor only.
Workpiece must be securely closed in the chuck.
Machine guard must be set to the correct position.
Tools must be sharpened and set up correctly.
Correct machine speed must be selected.
Different sizes and shapes cutting tools are used to remove material as needed.
By controlling the X,Y & Z axis, the machine can be used to accurately cut out areas such as slots.
Useful websites:
Technology student: vertical miller
BBC bitesize
DT online: vertical milling machine
Common operations:
Plain milling/ surface milling:
(this the the most common operation) this is performed to the flat, horizontal surface, parallel to the cutter.
Face milling
Removing material from the top face of the workpiece
Side milling
Removing material from the side of the workpiece
Shoulder milling
Removing material from the side of a workpiece
Boring/ hole expansion drilling
Enlarging an existing drilled hole
Tapping
adding a screw thread to a pre-drilled hole

## Slide 9
Metal Joining processes (permanent) Knowledge organiser
WJEC Engineering
MIG Welding
Metal Inert Gas welding for joining smaller, thinner pieces of steel.
Arc Welding
Used to join steel in medium to large projects, with thicker material. The consumable electrode is pushed against the joint and creates a current to join the metals.
Brazing
Joining steel to steel or other metals. Uses a brass filler metal called a brazing rod
Soldering
Uses a tin alloy to solder wither electronic components to a PCB (printed circuit board) or soldering copper pipe together
Oxy-Acetylene Welding
A high temperature welding process used to join steel by melting the two pieces together and pushing in a filler wire to the joint.
Pop riveting
Thinner metals can be joined using this process where a rivet is pushed through a hole in both materials then squeezed to expand and hold the joint
Key words:
Capillary action= Where solder flows into gaps when heated
Filler metal: the metal used to fill the joint between two materials, e.g. solder
Flux= Applied to a joint prior to welding or soldering. It chemically cleans the joint as it melts and helps the filler material to flow into the joint.

## Slide 10
Clips
There are lots of different clip fastenings. These are used to temporarily hold parts together for easy disassembly without tools,. Eg. road works signs.
Metal Joining processes (temporary) Knowledge organiser
WJEC Engineering
Nuts, bolts and screws
The sizes for these are metric e.g. M8 which means 8mm
Machine screws are used in pre-threaded metal holes and have a flat bottom, unlike wood screws.
Bolts are used on drilled holes. They pass all the way through and are secured with nuts. Hex bolts are the most common
Washers are used to distributor the load/ pressure applied on a material from a nut and bolt.
Nuts are used to secure a bolt or machine screw in place. Nylon lock nuts have piece of nylon in to prevent them from vibrating loose
Pg 2 of 2
Riveting
Riveting (e.g. pop-riveting) is often a permanent method, but as they are made of a dofter metal and can be drill out, they are referred to as temporary too.
Temporary vs permanent joining methods
Key words:
Fabrication= joining materials together
Assembly: Putting things together
Disassembly: Taking things apart
Dismantle: take apart into separate pieces.
TYPES OF BOLTS
Round head
Countersunk head
TYPES OF SCREWS
Flat washer
Split washer
Split washers are designed to stop nuts from vibrating loose
TYPES OF WASHERS
Temporary joints:
Can be dismantled without breaking the assembled parts.
Is useful when frequent assembly and disassembly is required.
Often easier and more cost-effective to carry out inspection, maintenance and repair as parts can be disassembled without breaking.
Lower strength joint
Often not a leak proof joint
Permanent joints:
Cannot be dismantled without breaking the assembled parts.
Is useful when the joint is intended to stay fixed for longer.
Maintenance and repair as more difficult as parts cannot be disassembled without breaking.
Stronger joint
Mostly create a leak proof joint

## Slide 11
Sand casting
Stock form used: ingots
Material used: most commonly
Metal casting processes Knowledge organiser
Products made by vacuum forming include:
Die casting
Stock form used: ingots
Material used: most commonly aluminium
A wooden pattern is placed inside the drag.
Fill with petrabond sand
Turn over and remove pattern
Place runner and riser pins in the cope and fill with petrabond sand. Add core for hollow parts
Place the cope on top of the drag
Remove runner and riser pins
Melt metal and pour into cavity
The process of pouring molten metals into a mould is called casting.
Advantages of casting are:
Large hollow shapes can be produced
Intricate shapes can be produced
Little to no waste is produced
A high quality surface finish can be produced (sand casting)
Keywords:
Molten: the melted state of metal
Die: A mould made from high carbon steel used in die casting
Cavity: empty space
Sprue: Where melted material enters the cavity. This needs to be removed from the finished part.
Sand casting is a repeatable process used in batch production, but will leave a textured surface which has to be finished. More suitable for simple, solid parts
pattern
Cast version
Core was placed
Die casting is a mass production process which creates highly detailed products.
The die is made from high carbon steel and produced a self-finished product and can be used repeatedly without losing accuracy, but is very expensive to make. This means that dies casting is cost effective when used to make large batches of a product
A pre-made die is fitted on the machine
Metal is melted then poured into the hopper
A plunger pushes the molten metal into the cavity
Mould is allowed to cool
Ejector pins push the die open and the finished part is removed
Sprue is cut off.

## Slide 12
Injection moulding
Stock form used: thermoplastic or thermoset granules or powder
This process involved forcing melted plastic into a mould. This process is accurate, good for high volume production (e.g. mass production) and produces little waste. However it is a very expensive process to set up.
Products that have been injection moulded need minor finishing, such as trimming the sprue or the ‘bleed’( lines where the two mould meet).
Plastic moulding processes Knowledge organiser
WJEC Engineering textbook
Plastics are shaped and moulded in many different ways to create complex shapes. To shape and mould plastics they must be heated until soft then they will harden when they cool.
Plastics are self-finishing which means they do not need to be sanded and polished unless they have been cut. The interior surface of the mould used in the process will determine whether the plastic has a textured or smooth finish as well as a gloss or matte finish texture.
Products made by injection moulding include
Lego blocks
Staplers
Product casings
Injection moulded lego in one half of its mould.
Hopper where the polymer granules are poured
Heat melts the polymer granules
Screw thread moves the melted plastic forwards
Finished product when the two halves of the mould separate and the plastic sprue is cut off
Identifiers:
Detailed designs
Seam line where the moulds halves met
Varying wall thickness
Feed points or ejector pin marks
Keywords:
Sprue: the mark on a finished product which shows where the plastic entered the mould
sprue

## Slide 13
Vacuum forming
Stock form used: thermoplastic sheets
Plastic moulding processes Knowledge organiser
WJEC Engineering textbook
Products made by vacuum forming include:
Car dashboards
Packaging
Suitcases
Rotational moulding
Stock form used: thermoplastic granules or powder
The former used for vacuum forming must have angled side (draft angles)to allow it to be easily removed from the finished plastic shape
Products made by rotational moulding include:
Bins and containers
Cones and barriers
Toys
Suitable former is manufactured
The former is placed in the vacuum former
Plastic sheet is placed above the former and clamped securely
The heater is turned on to heat the plastic sheet
The plastic becomes flexible
The air is pumped out of the area below the plastic and former
✅
❌
Vacuum forming is an inaccurate, low setup and running cost, low-volume process
Rotational moulding is inaccurate, low running cost, high set up cost and good for larger objects.
Identifiers:
Hollow objects
Seam line where the moulds halves met
Thicker walls