## Slide 1
Briefs, Specifications, ideas and development
Design Briefs
A Design Brief is the statement of how you will solve the Design Problem It will often include:
Constraints/ limitations
What the product is
Materials/processes
Any key information you know
Design Specifications
A Design Specification is a list of requirements your product has to meet in order to be successful
It is also useful for evaluation. If your product hasn’t met the Spec then it gives you a starting point for improvements.
Aesthetics | What the product looks like? Style? Colour Scheme? Design Movement?
Customer | Who would buy it? (Age, gender, socio-economic, personality) How does the design appeal to them?
Cost | How much will it cost? (min-max) Why?
Environment | Where will it be used? Why? How will you make it suitable?
Safety | How is it safe? How will it be checked? Why must it be safe?
Size | What is the maximum or minimum size? Why?
Function | What does the product do? What features make it do that function well? How is it unique from similar products?
Materials | What is it made from? Why?
Manufacture | How might it be made? Why? What scale of production? Why?
Technique | Description/ notes | Diagram
Orthographic Projection/ Working Drawings | Includes “Front”, “Plan” and “End” 2D Views, and often an Isometric 3D View Standardised method for scale, dimensions and line types Great for manufacturing | 
Isometric | Common 3D sketching method Can be drawn free-hand or using isometric paper and ruler Angles are at 30 degrees Great for seeing most of the products | 
1-Point Perspective | A 3D drawing method Often used by interior designers and architects Gives drawings depth Only uses 1 vanishing point | 
2-Point Perspective | Used for 3D designs Exaggerates the 3D effect Objects can be drawn above of below the horizon line but must go to the 2 vanishing points | 
Annotated Drawings/ Free and Sketches | Quick and easy way of getting ideas down Range of ideas can be seen Annotation helps explain designs further | 
Exploded View | Helps see a final design of a product and all it’s parts Can see where all the parts fit Great for manufacturers | 
Modelling and Development
Modelling and development are key to testing and improving products
This can be done physically using materials like; card, foam, clay, man-made boards or virtually in CAD
Modelling helps the designer get feedback from the customer, check aesthetics, function, sizes and even materials and production methods and change them if needed