## Slide 1
Hardwoods come from Deciduous Trees. These trees loose leaves in winter and grow fruit and flowers in spring |  | 
Material | Key info | Examples
Ash | Flexible, tough and shock resistant | Sports equipment Tool Handles
Beech | Fine finish, tough and durable | Toys, furniture and veneers
Mahogany | Easily worked, durable, high quality finish | High-end furniture
Balsa | Very soft and spongy. Light | Modelling
Oak | Tough, durable and hard | Flooring, furniture and veneers
Softwoods come from Coniferous Trees. These have thin, needle-like leaves and grow all year round. Often have pine cones and sometimes nuts and seeds |  | 
Material | Key info | Examples
Larch | Durable, tough, good water resistance and finishes well | Furniture, flooring and used outdoors
Pine | Light, easy to work with but can split | Cheap furniture, construction and decking
Spruce | Easy to work with, high stiffness but can decay quickly | Furniture, musical instruments and construction
Softwoods are generally cheaper than hardwoods as they are more available, since they grow quicker.
But because man-made boards are manufactured they are cheaper than timbers. Man-made boards also come in a better variety of sizes since they don’t depend on tree growth.
Stock forms for both include; sheets, dowel, planks, etc
Manufactured boards are made from wood chips/dust/ layers and glue. |  | 
Material | Key info | Examples
Chipboard | Prone to chipping but good compressive strength. Not-water resistant | Flooring, low-end furniture, flat-pack
MDF | Rigid and stable. Easy to finish. Absorbs liquid easily | Flat-pack furniture and kitchen unites
Plywood | Very stable. Exterior veneer can be used from more expensive woods | Shelving, furniture, toys
Trees are cut then converted into planks by cut using saws
It is then seasoned to reduce the moisture in the wood. This is done by either:
Air-drying – Planks are stacked and air allowed to circulate; causing evaporation
Kiln-drying – Where planks are put into a kiln and dried rapidly. This process is more costly than air-drying
Manufactured boards can be either be made by lamination or compression
Lamination – Layers of woods and adhesive are layered and compressed together. Usually with a more expensive wooden veneer on the top
Compression – Wood is shredded, heated and compressed with adhesive under extreme pressure
Woods and Boards
Natural Timbers
Man-Made Boards
Primary Processing of Papers and Boards